## Slide 1: TRANSNORTHERN
METROLINER 16,000 lbs DIFFERENCES TRAINING

## Slide 2: References:
Far 135.347
Ac_120-53b
TNA training manual 1.7.5.2:
“TransNorthern Aviation has evaluated its aircraft and identified Level A differences only. These differences will be instructed in module 4.5.3.3, Differences Training and recorded on form 5.14, Special Subjects.”

## Slide 3: 16,000 lbs metro:
N75TN (N175SW)
SERIAL NUMBER: AC-621B
CERTIFIED UNDER SFAR 41
NORMAL CATEGORY
LARGE NON-TRANSPORT
Notes: Insert pic of airworthiness certificate.

## Slide 4: Limitations
14,500 lbs Metro (KIAS)
Vmo: 246 / Mmo: 0.52
Va: 176
Vlo: 176
Vle: 173
Vfe (1/4): 214
Vfe (1/2): 179
Vfe (full): 159
Vmca: 87
Vsse: 115
16,000 lbs Metro (KIAS)
Vmo: 246 / Mmo: 0.52
Va: 185
Vlo: 175
Vle: 175
Vfe (1/4): 215
Vfe (1/2): 185
Vfe (full): 160
Vmca: 91
Vsse: 115

## Slide 5: Limitations
16,000 lbs Metro:
14,500 lbs Metro:

## Slide 6: Limitations
14,500 lbs Metro
MRW: 14,600 lbs
MGTW: 14,500 lbs
MLW: 14,000 lbs
MZFW: 13,130 lbs
MAX FWD BAGGAGE COMP: 800 lbs
MAX AFT BAGGAGE COMP: 850 lbs
MAX FLOOR LOADING: 150 LBS / ft2
16,000 lbs Metro
MRW: 16,100 lbs
MGTW: 16,000 lbs
MLW: 15,500 lbs
MZFW: 13,900 lbs
MAX FWD BAGGAGE COMP: 800 lbs
MAX AFT BAGGAGE COMP: 850 lbs
MAX FLOOR LOADING: 150 LBS / ft2

## Slide 7: Fuselage Bending moments

## Slide 8: Limitations
Maximum fuel imbalance for takeoff and landing is:
200 pounds when total fuel is greater than 2,000 pounds.
400 pounds when total fuel is less than 2,000 pounds.

## Slide 9: Misc. differences
RMI VOR NEEDLE #1 IS NOT CONNECTED.
RMI VOR NEEDLE #2 IS CONNECTED TO #2 VOR (SIC).
ONE ADF INSTALLED ON LOWER CENTER COLUMN.
ENGINE FIRE WARNING LIGHTS INSTALLED ABOVE DASHBOARD.

## Slide 10: MISC. DIFFerences

## Slide 11: Cawi limitations
14,500 Metro: 8 gallons minimum quantity
16,000 Metro: 9 gallons minimum quantity
For weight & balance, CAWI must be considered:

## Slide 12: CAWI performance
At what temperature do we have to start reducing takeoff weight?
ANC, FAI, long runways
Sea Level
16,000 lbs
Dry, Bleed Air OFF (Figure 4D-2)
ANSWER: +23 C
ANC, FAI long runways
Sea Level
16,000 lbs
Wet (Figure 4E-2)
ANSWER: +37 C

## Slide 13: CAWI performance
At what temperature do we have to start reducing takeoff weight?
DUT 4,500’ runway
Sea Level
Calm wind
16,000 lbs
Dry, Bleed Air OFF (Figure 4D-11)
ANSWER: +12 C
DUT 4,500’ runway
Sea Level
Calm wind
16,000 lbs
Wet (Figure 4E-11)
ANSWER: +25 C

## Slide 14: Limitations (Cawi)

## Slide 15: Limitations (Cawi)

## Slide 16: Cawi system pre-flight check

## Slide 17: Cawi system check

## Slide 18: Cawi normal takeoff

## Slide 19: Cawi normal takeoff (cont.)

## Slide 20: Cawi normal takeoff (cont.)

## Slide 21: Cawi normal takeoff (cont.)

## Slide 22: Afm performance section

## Slide 23: Afm performance section

## Slide 24: Afm performance section
Obtain Vref for a landing with ice on wings:
Conditions:
OAT -10 C
Sea Level
15,000 lbs
ANSWER: Vref = 134 KIAS

## Slide 25: Nose wheel steering

## Slide 26: Weight & balance (Sample ups anc-adq)
14,500 lbs Metro
Aircraft empty weight: 8,989 lbs
Fuel: 2,100 lbs
Pilots: 360 lbs
Available payload for UPS: 3,051 lbs
16,000 lbs Metro
Aircraft empty weight: 9,206 lbs
Fuel: 2,100 lbs
Pilots: 360 lbs
Available payload for UPS: 4,287 lbs
(Note, company policy is 3,000 lbs)

## Slide 27: Weight & balance (Sample ADQ-anc, fishload)
Aircraft empty weight: 8,989 lbs
Fuel: 1,300 lbs
Pilots: 360 lbs
Available payload for Fish backhaul:
13,130 – 8,989 – 360 = 3,781 lbs
Aircraft empty weight: 9,206 lbs
Fuel: 1,300 lbs
Pilots: 360 lbs
Available payload for Fish backhaul:
13,900 – 9,206 – 360 = 4,334 lbs
14,500 lbs Metro
16,000 lbs Metro

## Slide 28: List of supplements

## Slide 29: Fdr pre-flight check